## Slide 1: Beginning with FreeSurfer
and getting ready for ExploreDTI
They are both in versacea@10.145.65.122:/data/Phillips2/projects/dtistudy/BIOS/script

## Slide 2
http://sites.cardiff.ac.uk/cubric/cubric-users/user-documentation/mri-resources/mri-how-to/using-exploredti-via-the-command-line/
ExploreDTI in command line

## Slide 3
Resampling T1 image into DWI voxel size (2mm^3).
Generating the DWI.mat file with customized parameters (not sure how you can enter these?)
Getting to set the parameters before starting with correcting procedures. Automated Masking
SM/EC/EPI correction
Correcting the DWIs for Subject Motion (SM), Eddy Current (EC) and EPI distortions. I attached a txt file with all these settings to be entered in the command line of SM_EC_EPI_correction.
Extracting the DWIs.nii and DWIs.bvec from the SM_EC_EPI_DWI.mat file to reconstruct the fibers (TRACULA).
Whole-brain tractography (DTI)
Create Connectivity Matrices
Analytic Flow

## Slide 4
# First change LIA to RAS.
${MRI_CONVERT} ${BFS}/${SUBJECT}/mri/brain.mgz ${EXPLOREDTI}/T1_1mm_RAS/${SUBJECT}_T1_masked_RAS.nii --out_orientation RAS
# To enable parallel computation to use ExploreDTI
matlabpool(n_workers) (??8??);
# To disable: matlabpool close
-------------------------------------------------------------------------------------------------------------------
#From now on use ExploreDTI in : the most of the scripts are in /data/Phillips2/projects/dtistudy/ExploreDTI/Source/Plugins/
### I don’t want the software ExploreDTI to be in the dtistudy folder, please move it where you think is more convenient####.
---
# Resample the T1 image.
script: E_DTI_Resample_nii.p (or ??? E_DTI_Resample_nii_ex.p or E_DTI_Resample_nii_ex_me.p or E_DTI_resample_nii_file.p ??? NOT SURE WHICH ONE IS THE CORRECT ONE)
input: ${EXPLOREDTI}/T1_1mm_RAS/${SUBJECT}_T1_masked_RAS.nii
destination/output: ${EXPLOREDTI}/REORDERED/${SUBJECT}_T1.nii
voxel size: [2 2 2]
Resampling T1 image (${BFS}/${SUBJECT}/mri/brain.mgz) into DWI voxel size (2mm^3).

## Slide 5
GUI: Resampling T1 image (${BFS}/${SUBJECT}/mri/brain.mgz) into DWI voxel size (2mm^3).

## Slide 6
# script: E_DTI_convert_nii_dic_2_txt.p
# input and output destination folder: ${EXPLOREDTI}/REORDERED/.
?? Script to Convert folder of DICOMs to an ExploreDTI .mat file:
script syntax: E_DTI_Script_Get_DTI_folders(source_dir,target_dir)
source_dir = /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/REORDERED
target_dir = /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/REORDERED
NOT SURE HOW YOU CAN ENTER THE FOLLOWING PARAMETERS (NEXT SLIDE)?
Generating the DWI.mat file with customized parameters

## Slide 8
script: E_DTI_SMECEPI_Main(parameter_filename);
destination folder: /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/MC_D_EPI/
mv /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/MC_D_EPI/*trafo.mat /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/MC_D_EPI/trafo/.
mv /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/MC_D_EPI/*native.mat /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/MC_D_EPI/native/.
Setting the parameters/ Correcting the DWIs for Subject Motion (SM), Eddy Current (EC) and EPI distortions

## Slide 9
GUI to set the parameters before starting with correcting procedures. These will probably be defined all at once in the command line.
Automated Masking
SM/EC/EPI correction

## Slide 11
GUI to set the parameters before starting with correcting procedures. These will probably be defined all at once in the command line.
Automated Masking
SM/EC/EPI correction

## Slide 12
For native space=4
For transformed data=4

## Slide 17
Extracting the DWIs.nii and DWIs.bvec from the SM_EC_EPI_DWI.mat file to reconstruct the fibers (TRACULA).
Script??
Source folder: /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/MD_C_EPI/trafo/.
Destination folder: /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/DWIs/.
------
mv /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/DWIs/${SUBJECT}_MD_C_trafo_grads.txt /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/DWIs/61directions/.
/data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/DWIs/61directions/convertGrads.sh . ..
# now *_MD_C_trafo_grads68.txt should look like this:
mkdir /data/Phillips2/projects/dtistudy/BIOS/data/tracula/${SUBJECT}/orig
mv /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/DWIs/${SUBJECT}_MD_C_trafo_DWIs.nii /data/Phillips2/projects/dtistudy/BIOS/data/tracula/ ${SUBJECT}/orig /.
mv /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/DWIs/${SUBJECT}_MD_C_trafo_grads68.txt /data/Phillips2/projects/dtistudy/BIOS/data/tracula/ ${SUBJECT}/orig /.

## Slide 19
Other example
bval211

## Slide 20: Now with TRACULA, run trac-all
trac-all –c /data/Phillips2/projects/dtistudy/BIOS/data/tracula/scripts/dmrirc.${SUBEJCT} –prep
trac-all –c /data/Phillips2/projects/dtistudy/BIOS/data/tracula/scripts/dmrirc.${SUBEJCT} –bedp
trac-all –c /data/Phillips2/projects/dtistudy/BIOS/data/tracula/scripts/dmrirc.${SUBEJCT} –path
# Here is an example of the script needed for each subject:
# All the subjects will need a dmrirc file.
# I usually, just sed ‘s/20120303.1953/${SUBEJECT}/g’

## Slide 21
Going back to ExploreDTI (in parallel) run whole-brain tractography (DTI)
WholeBrainTrackingDTI(filename_in, filename_out, parameters);
With the following parameters: paramaters.SeedPointRes = [3 3 3] paramaters.StepSize = 1 paramaters.FAThresh = 0.2000 paramaters.AngleThresh = 45 paramaters.FiberLengthRange = [50 500]
Source & Destination folder: /data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/MD_C_EPI/trafo/.

## Slide 22
And Create Connectivity Matrices
E_DTI_Network_analysis_exe(dti_filename,tracts_filename,img_filename,A_T,A_L,L,VDims_A,mat_dir,img_suffix,selected_labels,ACh);
dti_filename = name of the DTI .mat file
#/data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/MD_C_EPI/trafo/*MD_C_trafo.mat tracts_filename = name of the DTI tracts .mat file
#/data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/MD_C_EPI/trafo/*MD_C_trafo_Tracts_DTI.mat img_filename = [] # for now A_T = 3D volume of the atlas (e.g. AAL) reference template. Note this volume must be read into MATLAB using the command:A_T=E_DTI_load_nii(‘template_filename’)
#/data/Phillips2/projects/dtistudy/ExploreDTI/Templates/AAL_Template.nii A_L = 3D volume of the atlas (e.g. AAL) labels. As above, the volume need to be loaded into MATLABA_L=E_DTI_load_nii(‘labels_filename’) #/data/Phillips2/projects/dtistudy/ExploreDTI/Templates/AAL_Labels.nii L = cell array of label names for each region in A_L.
#/data/Phillips2/projects/dtistudy/ExploreDTI/Templates/AAL_Label_Names.txt mat_dir = Directory to save the connectivity matrices
#/data/Phillips2/projects/dtistudy/BIOS/data/exploreDTI/CMs img_suffix = [] # for now. selected_labels = a n_labelsx2 matrix of pairs of label indices to create an individual tract .mat file for that pair of labels. Use [] to disable. Use nchoosek(1:n_atlas_labels,2) to output for every pair of labels # for now. ACh = 3